AC-Delco Alternator Windmill

Written By: Thomas G (08/2014)
Feel free to use: no strings attached (text content only / images respectfully referenced)

# INTRODUCTION

# Materials
- Hardware
  - Double 5” Lap Vinyl Siding [ $7.95 @ 12-feet ]	https://www.homedepot.com/p/Double-5-in-x-144-in-Beige-Vinyl-Lap-Siding-PC50NBH/302174965

  - (8) DIN rail, slotted, 35mm x 10mm x 1M Long Aluminum Rails [ $32 ($8.00/2-pack@1M) ]
    - https://www.automationdirect.com/adc/Shopping/Catalog/Enclosures_-z-_Subpanels_-z-_Thermal_Management_-z-_Lighting/Enclosure_Parts_-a-_Accessories/Internal_Component_Mounting_Accessories/DIN_Rails/DN-R35SAL1-2
    - OR get 10 for [ $36.00 ]
    - https://www.automationdirect.com/adc/Shopping/Catalog/Enclosures_-z-_Subpanels_-z-_Thermal_Management_-z-_Lighting/Enclosure_Parts_-a-_Accessories/Internal_Component_Mounting_Accessories/DIN_Rails/DN-R35SAL1

  - 1” EMT Conduit Pipe sold @ 10-feet [ $7.25 @ 10-feet ]	https://www.homedepot.com/p/1-in-EMT-Conduit-101568/100400409
    - 1-3/16” (1.1875”) inside diameter measured
    - 1-4.5/16” (1.2813”) outside diameter measured
    - See https://creativeshelters.com/fittings/diameter

- 3D Printed Parts
  - Gear-1 = 108 Grams = $2.43

# Assembly Instructions

## Frame
- Attach (2) DIN Rails to the Post-Mount.stl
  - Center Post-Mount around Din Rail Slot # 10
  - Align first screw hole in DIN Rail Slot #9
  - Align second screw hole in DIN Rail Slot #11
  - (2) #10-24 x 3/4” machine screws & nuts