AC-Delco Remy Alternator Windmill

Written By: Thomas G (08/2014)
Feel free to use: no strings attached (text content only / images respectfully referenced)

# INTRODUCTION
## Specifications

Gear Ratios
Name	Input	Output	Ratio	Rotation
Hub-Gear	Blades	26 Outside Gears	1:1 ( x1 )	Clockwise
Gear-1	26 Outside Gears	14 Inside Gears	13:7 ( x0.5385 )	Counter / Clockwise
Gear-2	14 Inside Gears ( Gear-1 ) / 22 Gears	22 Gears / 8 Gears ( Gear-3 )	4:7 ( x1.75 )	Clockwise
Gear-3	8 Inside Gears	26 Outside Gears	4:13 ( x3.25 )	Counter / Clockwise
Gear-4	13 Inside Gears	26 Outside Gears	1:2 ( x2 )	Clockwise
Gear-5	18 Inside Gears	26 Outside Gears	9:13 ( x1.44 )	Counter / Clockwise
Gear-6 / Alternator	26 Outside Gears ( Gear-5 )	11 Alternator Gears	26:11 ( x2.36 )	Clockwise

  - Total Ratio = Gear-Up x 20.8152

# Materials ( $183.76 )

## Hardware Materials ( $51.20 )

- Double 5” Vinyl Lap Siding [ $7.95 @ 12-feet ]
  - Purchase @ https://www.homedepot.com/p/Double-5-in-x-144-in-Beige-Vinyl-Lap-Siding-PC50NBH/302174965

- (8) Aluminum DIN Rails - 35mm x 10mm x 1M, slotted [ $32 ($8.00/2-pack@1M) ]
  - Purchase @ https://www.automationdirect.com/adc/Shopping/Catalog/Enclosures_-z-_Subpanels_-z-_Thermal_Management_-z-_Lighting/Enclosure_Parts_-a-_Accessories/Internal_Component_Mounting_Accessories/DIN_Rails/DN-R35SAL1-2

  - OR get 10 for [ $36.00 ]
  - Purchase @ https://www.automationdirect.com/adc/Shopping/Catalog/Enclosures_-z-_Subpanels_-z-_Thermal_Management_-z-_Lighting/Enclosure_Parts_-a-_Accessories/Internal_Component_Mounting_Accessories/DIN_Rails/DN-R35SAL1

- 1” EMT Conduit Pipe sold @ 10-feet [ $7.25 @ 10-feet ]
  - Purchase @ https://www.homedepot.com/p/1-in-EMT-Conduit-101568/100400409
  - 1-3/16” (1.1875”) inside diameter measured
  - 1-4.5/16” (1.2813”) outside diameter measured
  - See https://creativeshelters.com/fittings/diameter

## Power Materials ( $112.43 )

- (3) 6Vdc Lead Acid Batteries [ $8.64/ea = $25.92 ]
  - https://www.walmart.com/ip/American-Hunter-DE645DC-6V-4-5A-HR-Rechargeable-Battery/40369551

- Solar Inverter 10.8Vdc to 30Vdc Grid Tie [ $86.51 ]
  - https://www.aliexpress.com/item/500w-on-grid-tie-solar-power-inverter-12v-24v-input-dc-to-home-voltage-220v-110v/32822544294.html

## Plastic Filament for 3D-Prints ( $33.05 )

- 3D Printed Parts [ $20.13] ( Front to Back )
  - Hub	=	260 grams	=	$5.85
  - Hub-Gear	=	207 grams	=	$4.66
  - Gear-1	=	256 Grams	=	$5.76
  - Gear-2	=	104 Grams	=	$2.34
  - Gear-3	=	152 Grams	=	$3.42
  - Gear-4	=	202 Grams	=	$4.54
  - Gear-5	=	232 Grams	=	$5.22
  - Gear-6 ( Alternator )	=	56 Grams	=	$1.26
  - Hub-Mount = 77 Grams = $1.73
  - Alt-Lower-Mount = 219 Grams = $4.95
  - Post-Mount = 133 Grams = $2.99

# Assembly Instructions

## Frame

1. Connect (2) DIN Rails together with Post-Mount.stl
  1. Insert #10 Nuts into the side slots of the Post-Mount ( may require pounding in with a hammer and punch )
  2. Position Post-Mount between 2-DIN Rails centered around Slot #10 of both rails
    1. One side-hole at Slot #9
    2. One side-hole at Slot #11
  3. Insert (2) #10-24 x 3/4” machine screws on Non-Gear Side

1. Install Gear-2 and Gear-2-Standoff
- Attach (2) DIN Rails to the Post-Mount.stl
  - Install #10 Nuts into the Post-Mount
  - Center Post-Mount around Din Rail Slot # 10
  - Align first screw hole in DIN Rail Slot #9
  - Align second screw hole in DIN Rail Slot #11
  - (2) #10-24 x 3/4” machine screws & nuts

- Insert Nut in Hub-Mount
  - Insert Nut in Hub-Mount
  - Drive in (2) #10-24 x 3/4” machine screws & nuts in very back of 1st slot into Hub-Mount
  - Align second DIN ( Gear DIN ) to Hub-Mount on the right? side
  - Drill through both DIN rails where 5/16” bolt will go
  - Turn Over
  - Drill through the DIN rail so 5/16” bolt can come through other side
  - Insert 5/16” Bolt

- Setup Brace DIN
  - Drill out back of the 1st slot for 5/16” Bolt

- Install first Gear
  - Insert 5/16” x 5” bolt through Brace DIN, Gear DIN
  - Through Washer
  - Through Gear-1
  - Through Gear-1-Spacer
  - Through Hub-Mount

- Install Second Gear FIRST
  - This allows the Hole for the 1st Gear to be drilled correctly