AC-Delco Remy Alternator Windmill

Written By: TGit-Tech (12/2017)
Feel free to use: no strings attached (text content only / images respectfully referenced)

# INTRODUCTION
## Specifications

Gear Ratios
Name	Input	Output	Ratio	Rotation
Hub-Gear	Blades	26 Outside Gears	1:1 ( x1 )	Clockwise
Gear-1	26 Outside Gears	14 Inside Gears	13:7 ( x0.5385 )	Counter / Clockwise
Gear-2	14 Inside Gears ( Gear-1 ) / 22 Gears	22 Gears / 8 Gears ( Gear-3 )	4:7 ( x1.75 )	Clockwise
Gear-3	8 Inside Gears	26 Outside Gears	4:13 ( x3.25 )	Counter / Clockwise
Gear-4	13 Inside Gears	26 Outside Gears	1:2 ( x2 )	Clockwise
Gear-5	18 Inside Gears	26 Outside Gears	9:13 ( x1.44 )	Counter / Clockwise
Gear-6 / Alternator	26 Outside Gears ( Gear-5 )	11 Alternator Gears	26:11 ( x2.36 )	Clockwise

  - Total Ratio = Gear-Up x 20.8152

# Materials ( $205.11 )

## Hardware Materials ( $51.90 )

- (2) Double 5” Vinyl Lap Siding [ $7.95 @ 12-feet ]
  - Purchase @ https://www.homedepot.com/p/Double-5-in-x-144-in-Beige-Vinyl-Lap-Siding-PC50NBH/302174965

- (10) Aluminum DIN Rails - 35mm x 10mm x 1M, slotted [ $36/10-pack ]
  - Purchase @ https://www.automationdirect.com/adc/Shopping/Catalog/Enclosures_-z-_Subpanels_-z-_Thermal_Management_-z-_Lighting/Enclosure_Parts_-a-_Accessories/Internal_Component_Mounting_Accessories/DIN_Rails/DN-R35SAL1

- 1” EMT Conduit Pipe sold @ 10-feet [ $7.25 @ 10-feet ]
  - Purchase @ https://www.homedepot.com/p/1-in-EMT-Conduit-101568/100400409
  - 1-3/16” (1.1875”) inside diameter measured
  - 1-4.5/16” (1.2813”) outside diameter measured
  - See https://creativeshelters.com/fittings/diameter

## Fasteners

- (18) #10-24 x 1” Machine Screws & Lock Nuts
  - (15) Blades to Hub ( 3x per Blade-to-Hub with 5-blades )
  - (3) Hub to Hub-Gear

- (15) #10-24 x 1/2” Machine Screws & Wide #10x3/4” Flat Washers & Lock Nuts
  - (3) Per Vinyl-to-DIN x (5) Blades
## Power Materials ( $112.43 )

- (3) 6Vdc Lead Acid Batteries [ $8.64/ea = $25.92 ]
  - https://www.walmart.com/ip/American-Hunter-DE645DC-6V-4-5A-HR-Rechargeable-Battery/40369551

- Solar Inverter 10.8Vdc to 30Vdc Grid Tie [ $86.51 ]
  - https://www.aliexpress.com/item/500w-on-grid-tie-solar-power-inverter-12v-24v-input-dc-to-home-voltage-220v-110v/32822544294.html

## 3D-PLA Filament ( $40.78 )

- 3D Printed Parts ( Prices are based on $14.99 per 1Kg Spool of PLA )
  - Drive Train – Front to Back ( $27.54 )
    - Hub	=	260 grams	=	$4.87	= (3) #10-24 x 1” Bolts & Nuts
    - Hub-Gear	=	209 grams	=	$3.92	= (1) 5/16” x ? Bolt & (2)Nuts
    - Gear-1	=	256 Grams	=	$4.80	= (1) #10-24 x 2” Bolt & (2)Nuts & (2)5/16” Flat Washers
    - Gear-2	=	69 Grams	=	$1.29	= (1) #10-24 x 2” Bolt & (4)Nuts & (2)5/16” Flat Washers
    - Gear-3	=	152 Grams	=	$2.85	= (1) #10-24 x 2” Bolt & (2)Nuts & (2)5/16” Flat Washers
    - Gear-4	=	202 Grams	=	$3.79	= (1) #10-24 x 2” Bolt & (2)Nuts & (2)5/16” Flat Washers
    - Gear-5	=	232 Grams	=	$4.35	= (1) #10-24 x 2” Bolt & (2)Nuts & (2)5/16” Flat Washers
    - Gear-6 ( Alternator )	=	86 Grams	=	$1.61	= Pulley Nut and Washer that comes with Alternator

  - Center Pieces – Front to back ( $6.90 )
    - Hub-Mount-26g	=	160 Grams	=	$3.00	= (2)#10-24 x 3/4” Bolts & Lock-Nuts, (1)5/16” x 6” Bolt & (2)Nuts
    - Post-Mount	=	140 Grams	=	$2.55	= (2)#10-24 x 3/4” Bolts & Nuts
    - Alt-UpperMount	=	69 Grams	=	$1.35	= (1)#10-24 x 3/4” Bolts & Nuts

  - Other Pieces ( $ 6.34 )
    - Alt-LowerMount	=	257 Grams	=	$4.78	= (2)#10-24 x 3/4” Bolts & Lock-Nuts
    - (5) Blade-NutHolders	=	83 Grams ( 17/ea )	=	$1.56	= (10)#10-24 x ? Bolts & Nuts & Lock-Nuts
    - Bolt-Drill-Guide
    - DIN Clamp	=	21 Grams	=	$0.39	= (2)#10-24 x 2” Bolts & Lock-Nuts

# Assembly Instructions

## Frame

1. Connect (2) DIN Rails together with Post-Mount.stl
  1. Insert #10 Nuts into the side slots of the Post-Mount ( may require pounding in with a hammer and punch )
  2. Position Post-Mount between 2-DIN Rails centered around Slot #10 of both rails
    1. One side-hole at Slot #9
    2. One side-hole at Slot #11
  3. Insert (2) #10-24 x 3/4” machine screws on Non-Gear Side

1. Install Gear-2 and Gear-2-Standoff
- Attach (2) DIN Rails to the Post-Mount.stl
  - Install #10 Nuts into the Post-Mount
  - Center Post-Mount around Din Rail Slot # 10
  - Align first screw hole in DIN Rail Slot #9
  - Align second screw hole in DIN Rail Slot #11
  - (2) #10-24 x 3/4” machine screws & nuts

- Insert Nut in Hub-Mount
  - Insert Nut in Hub-Mount
  - Drive in (2) #10-24 x 3/4” machine screws & nuts in very back of 1st slot into Hub-Mount
  - Align second DIN ( Gear DIN ) to Hub-Mount on the right? side
  - Drill through both DIN rails where 5/16” bolt will go
  - Turn Over
  - Drill through the DIN rail so 5/16” bolt can come through other side
  - Insert 5/16” Bolt

- Setup Brace DIN
  - Drill out back of the 1st slot for 5/16” Bolt

- Install first Gear
  - Insert 5/16” x 5” bolt through Brace DIN, Gear DIN
  - Through Washer
  - Through Gear-1
  - Through Gear-1-Spacer
  - Through Hub-Mount

- Install Second Gear FIRST
  - This allows the Hole for the 1st Gear to be drilled correctly
## Blades

- Cut Vinyl Siding
  - Cut Vinyl Siding into (5) 32” long sections

- Attach Vinyl Siding Sections to DIN Rails
  - Attach Each 32”-Vinyl Siding Section to a DIN Rail with (3)#10-1/2” + #10x3/4” Washer + Lock Nut
  - Be sure the Vinyl Siding is attached so the DIN Rail will mount to the Hub with the DIN Rail out front and the Siding angled backwards

- Attach Blades to Hub
  - Using a Blade-NutHolder for each Blade; attach each blade to the Hub with (3)#10-1” Machine Screw + Lock Nut

# Lessons Learned

## Why the 5/16” x 6” Bolt across the front?

Original designs showed the pressure from the hub driving the 90-degree angle produced more force than the outer DIN-Rail could handle effectively. The only vertical alignment support available is either behind all gears and the small #10 machine screws that goes through each gear. Since the #10 screws through the gears cannot be tightened due to gear clamping and there is no way to brace the outer DIN at the front and back. The long 5/16” Bolt keeps all front size DINs in vertical alignment while significant force is applied on the Miter gear.

## Why a 2-piece Hub?

First; There is no way to print the overhang required to keep the miter-gear tooth overlap from hitting the Blade slot supports. Thus the gap ( lifted hub ) is created using a Hub and Hub-Gear piece bolted together.

Second; Even if a model could be designed to address the miter-gear tooth overlap – The two piece design contains a hallow center and thus saves a substantial amount of plastic resources.

## Why the idle-gear design on 5-blade revision?

The most recent 3-blade design worked well in 40mph winds most of 5 or 6 hours. However; the design started to snap under heavy load and started to come apart first by slippage on the miter-gears ( Hub 90-angle ) in which there was miter-to-miter tooth skipping as well as 1st Gear to miter tooth skipping. The 5-blade design carries not only a better ( larger and tighter ) miter-gear connection by overlapping the miter-teeth but also introduced the idler-gear to eliminate the 1st Gear to angled miter gear which was also causing tooth skipping problems.

## Why 5-Gears instead of 3?

One reason for the 5-Gear was spacing for the new idler gear introduced in the 4.3 issue described above.

However, most importantly, the 5-Gear system was a result of getting the alternator back behind the post while allowing for exactly the 10” of blade clearance on the front. The goal was to have the smallest front over-hang as possible ( for support purposes ) that gave enough clearance to guarantee the blades never made contact with the post or a front mounted alternator ( which also caused blade-binding issues on previous designs ).

Allowing the maximum 10” clearance on the front for the blades required moving the alternator behind the post and thus required 5-Standard size gears to move the driving mechanism back. A belt or chain design was considered but to limit costs and possibly even enhance charging ability at a 20:1 ratio; the extra gearing was included.